## Slide 1: Fabrication/Assembly Instructions
Model T
Ver 0.4

## Slide 2: Overview

## Slide 3: McMaster Parts List
Ø1/8”, L3/8” dowel pin (P1)
  #97395A35 (8x)
Ø1/8”, L5/8” dowel pin (P2)
  #97395A445 (12x)
Nylon Pulley (J1)
  #3434T31 (12x)
Ø1/4”, L2-1/2” zinc-plated female standoffs (S1)
  #92474A029 (4x)

## Slide 4: 3D Printer Requirements
Current model only tested on Stratasys Dimension uPrint
  Layer thickness: 0.254 mm (0.010 in)
  Model material: ABS
  Support material? Yes
Not recommended to use PLA or alternative materials for RP parts
Majority of parts are designed to not require support material
Authors do not know how well alternate 3D printers will produce adequate components

## Slide 5: Finger Assembly - Prep
Hole Ream (Ø0.1240”, 3.15mm)
Tendon Through Hole (Ø1.5-2mm)
  ⊥ to surface

## Slide 6: Finger Assembly (x4)
Components:
  Rapid-prototype (RP) finger
  P2 (3x)
  J1 (1x)
Press-fit assembly
  Tendon holes should not be obstructed by pins P2 after assembly
Pin P2
Pulley J1

## Slide 7: Drive Block B1 Assembly
Components:
  B1.stl (2x)
  P1 (3x)
  J1 (2x)
Press-fit assembly
  Offset design should ensure that pulleys J1 spin freely after assembly

## Slide 8: Base Block B2 (2x) Assembly
Components (per block):
  B2.stl (1x)
  P2 (1x)
  J1 (1x)
Press-fit assembly
  Use shim with pulley J1 during assembly so that press-fit of pin P2 doesn’t cause sides of B2.stl to pinch on J1
  Pulley J1 should spin freely after assembly

## Slide 9: Differential Block B3 (2x) Assembly
Components (per block):
  B3.stl (2x)
  Pulley J1 (2x)
  Pin P1 (3x)
Press-fit assembly

## Slide 10: Motor Block B4 Assembly
Components:
  B4a.stl
  B4b.stl
  P1 (2x)
  J1 (2x)
Press-fit assembly
  Minor filing may be needed to ensure that pulleys spin freely after assembly
  Useful to use shim when assembling top pulley J1 to avoid pinching when pressing pin P1

## Slide 11: Motor Block Assembly
Components:
  Dynamixel MX-64
  PULLEY.stl
  M2 L2mm screw (2x)
  M2.5 L7.5mm screw (1x)
Block B4 may be attached with any appropriately-sized set of bolts/nuts
Improved clinch knot used in prototype tests to affix tendon to drive pulley

## Slide 12: Frame Assembly Overview

## Slide 13: Frame Top Assembly Overview
Top and bottom frame held by standoffs S1
Plates A1.stl and A2.stl clamp finger bases in fixed configuration
  Notches specify how A1 and A2 align with each other
Fixed tendons tied between fingers and differential block on same side of grasps
A1
A2
B3

## Slide 14: Frame Top Assembly - Fingers
Fingers inserted from above
  Slide down at an angle
  Snap into recesses on bottom layer of A2.stl
Fingers should snap rigidly in place
  In absence of fasteners or clamping

## Slide 15: Frame Top Assembly - Tendons
Tendon terminates at distal end of finger pairs
  Tendon should be pulled tight by joint stiffnesses
Helpful to pre-load fingers during tendon attachment for more slack
Tendon termination points

## Slide 16: Frame Bottom Assembly Overview
Motor block
A3
A4
B2 (2x)
B1
No fasteners needed for motor block
A3 and A4 used to clamp pulley blocks B2 in place
  Motor and B2 blocks should snap into place

## Slide 17: Final Frame Assembly
A1 snaps onto top of block B4 to pin frame in correct orientation
Standoffs S1 used to fix top and bottom frame assemblies
Final tendon attachment is performed at very end
  To simplify assembly, tendon between actuation pulley and drive pulley block B1 can be left slack

## Slide 18: Differential Tendon
Connect final actuation tendon between two differential blocks B3
  Route tendon through pulley blocks B2 and actuation pulley block B1
Tendon should be tied taut with actuation pulley block B1 pinned as close to the bottom frame as possible
  Fingers can be preloaded to provide additional slack to simplify tie-off

## Slide 19: Servo Actuation Zero
Actuation tendon between drive pulley and block B1 needs to be taut at servo zero position
Drive servo to zero position
Loosen M2, M2.5 attachment screws such that drive pulley spins loosely
Re-affix pulley in position where drive tendon is as taut as possible