## Slide 1
OpenHand
Model T
Version 0.5
Assembly Instructions
Last updated: November 11, 2013
Flexure Base
Pivot Base

## Slide 2: Parts List 1/3 (Flexure Base)
Part Name | Quantity | Usage | Vendor | Preview
a1_flexure.stl | 1 | Top Keeper Plate | 3D Print | 
a2.stl | 1 | Top Plate | 3D Print | 
a3.stl | 1 | Bottom Plate | 3D Print | 
a4.stl | 1 | Bottom Keeper Plate | 3D Print | 
b1.stl | 2 | Drive Pulley Block | 3D Print | 
b2.stl | 2 | Routing Base Block | 3D Print | 
b3.stl | 4 | Differential Block | 3D Print | 
b4_a.stl, b4_b.stl | 1 | Servo Block | 3D Print | 
b5.stl | 1 | Servo Pulley | 3D Print | 
d1.stl | 1 | Sunon Fan Clamp* | 3D Print | 
d2_a.stl, d2_b.stl | 1 | Case Shell* | 3D Print | 
* optional

## Slide 3: Parts List 2/3 (Flexure Base)
Part Name | Quantity | Usage | Vendor | Preview
finger_flexure_print.stl | 4 | Finger Molds – Breakaway | 3D Print | 
finger_ff_A.stl, finger_ff_B.stl, finger_ff_C.stl, shell_ff_A.stl, shell_ff_B.stl, shell_ff_C.stl | 4 | Finger Molds – Multi Part | 3D Print | 
Robotis MX-64 Dynamixel | 1 | Actuator | Robotis [link] | 
Sunon 25x10mm 12VDC Fan | 1 | Cooling Fan* | Digikey [link] | 
Power Pro Spectra | 1 | Tendon | Amazon [link] | 
PMC-780 Urethane | 1 | Finger Joint Urethane | Smooth-On [link] | 
Vytaflex 30 Urethane | 1 | Finger Pad Urethane | Smooth-On [link] | 
* optional

## Slide 4: Parts List 3/3 (Flexure Base)
Part Name | Quantity | Usage | Vendor | Preview
Ø1/8”, L3/8” steel dowel pin (J1) | 13 | Support Pin | McMaster [98381A470] | 
Ø1/8”, L5/8” steel dowel pin (J2) | 12 | Support Pin | McMaster [98381A472] | 
Ø3/8”, Wd1/8” nylon pulley (P1) | 12 | Tendon Routing | McMaster [3434T31] | 
Ø1/4”, L2-1/2” zinc-plated female standoff (S1) | 4 | Support | McMaster [92474A029] | 
Socket Cap Screw 8-32, L3/4” | 8 | Fastener | McMaster [91253A197] | 
M2.5, L7.5mm bolt | 1 | Fastener | Provided w/ Dynamixel | 
M2, L3mm bolt | 2 | Fastener | McMaster [91292A003] | 
2-56, L3/4” bolt/nut | 2 | Fastener | McMaster [92196A084] | 
* optional

## Slide 5: Parts List 1/3 (Pivot Base)
Part Name | Quantity | Usage | Vendor | Preview
a1_pivot.stl | 1 | Top Keeper Plate | 3D Print | 
a2.stl | 1 | Top Plate | 3D Print | 
a3.stl | 1 | Bottom Plate | 3D Print | 
a4.stl | 1 | Bottom Keeper Plate | 3D Print | 
b1.stl | 2 | Drive Pulley Block | 3D Print | 
b2.stl | 2 | Routing Base Block | 3D Print | 
b3.stl | 4 | Differential Block | 3D Print | 
b4_a.stl, b4_b.stl | 1 | Servo Block | 3D Print | 
b5.stl | 1 | Servo Pulley | 3D Print | 
c1.stl | 4 | Finger Pivot Base | 3D Print | 
d1.stl | 1 | Sunon Fan Clamp* | 3D Print | 
* optional

## Slide 6: Parts List 2/3 (Pivot Base)
Part Name | Quantity | Usage | Vendor | Preview
d2_a.stl, d2_b.stl | 1 | Case Shell* | 3D Print | 
finger_pivot.stl | 4 | Finger Molds – Breakaway | 3D Print | 
finger_fp_A.stl, finger_fp_B.stl, shell_fp_A.stl, shell_fp_B.stl, shell_fp_C.stl | 4 | Finger Molds – Multi Part | 3D Print | 
Robotis MX-64 Dynamixel | 1 | Actuator | Robotis [link] | 
Sunon 25x10mm 12VDC Fan | 1 | Cooling Fan* | Digikey [link] | 
Power Pro Spectra | 1 | Tendon | Amazon [link] | 
PMC-780 Urethane | 1 | Finger Joint Urethane | Smooth-On [link] | 
Vytaflex 30 Urethane | 1 | Finger Pad Urethane | Smooth-On [link] | 
* optional

## Slide 7: Parts List 3/3 (Pivot Base)
Part Name | Quantity | Usage | Vendor | Preview
Ø1/8”, L3/8” steel dowel pin (J1) | 13 | Support Pin | McMaster [98381A470] | 
Ø1/8”, L5/8” steel dowel pin (J2) | 12 | Support Pin | McMaster [98381A472] | 
Ø1/4”, L1” steel dowel pin (J3) | 4 | Joint Pin | McMaster [98381A542] | 
Ø3/8”, Wd1/8” nylon pulley (P1) | 12 | Tendon Routing | McMaster [3434T31] | 
Ø1/4”, L2-1/2” zinc-plated standoff | 4 | Support | McMaster [92474A029] | 
Socket Cap Screw 8-32, L3/4” | 8 | Fastener | McMaster [91253A197] | 
M2.5, L7.5mm bolt | 1 | Fastener | Provided w/ Dynamixel | 
M2, L3mm bolt | 2 | Fastener | McMaster [91292A003] | 
2-56, L3/4” bolt/nut | 2 | Fastener | McMaster [92196A084] | 
Torsion Spring, Ø0.34”, 0.028” wire diameter, 180˚, left-hand wound | 4 | Joint Return Spring | McMaster [9271K605] | 
* optional

## Slide 8: Part Preparation
Finger Molding
Consult DDM (Dieless Deposition Manufacturing) guide for further details on pouring/preparing the joints and pads for fingers
1
finger_flexure_print.stl
finger_pivot_print.stl

## Slide 9: Part Preparation
Ø 1.5±0.5 mm
finger_flexure_print.stl (x4)
Tendon Routing
2
Drill tendon routing holes such that tendon will run tangent to inserted pin. Minimize contact between tendon and ABS but ensure that tendon runs freely. For the pivot base design, the fingers also have a torsional spring mounting hole to be drilled as shown.
finger_pivot_print.stl (x4)

## Slide 10: Part Preparation
Tendon Routing (2/2)
3
Use helper_jig.stl to aid in positioning and orientation during drilling if desired. Routing holes should be drilled perpendicular to hole surface. The fingers are designed such that for each routing hole, there is at least one feature surface that is perpendicular to the direction of drilling, as shown above. It is ideal to minimize the diameter of the tendon routing holes if possible.
helper_jig.stl

## Slide 11: Part Preparation
Surface Filing/Deburring
4
File down and deburr bearing surfaces as indicated above. Ensure that no support material remains, if applicable. Complementary piece (ie. pulley, finger) should slide in freely. The parameter “print Free” in the CAD parameters file can also be adjusted to avoid this step. The default printing tolerances are calibrated to a Stratasys FDM printer.
b4_a.stl
b4_b.stl
b2.stl (x2)
finger_flexure_print.stl (x4)
c1.stl (x4)

## Slide 12: Part Preparation
Reaming (1/8” pin holes)
5
Use Ø0.1240” reamer to prepare pin holes as indicated above. This step can be skipped in lieu of precise 3D printer calibration and parameter selection, but manual reaming is the recommended approach.
b4_a.stl
b4_b.stl
finger_flexure_print.stl (x4)
finger_pivot_print.stl (x4)
b1.stl (x2)
b2.stl (x2)
b3.stl (x4)
c1.stl (x4)

## Slide 13: Part Preparation
Reaming (Pivot Bases)
6
Use Ø0.2490” reamer to prepare pin holes on pivot bases c1.stl, and Ø0.2510” reamer to prepare pin holes on the corresponding fingers finger_pivot.stl. Finger should spin freely and loosely on a Ø0.25” steel pin. The steel pin should fit tightly in part c1.stl with no slip.
Ø 0.2510 “
Ø 0.2490 “
finger_pivot_print.stl (x4)
c1.stl (x4)

## Slide 14: Assembly
Parts | 
Dynamixel MX-64 | 
d1.stl | 
Sunon 12VDC fan | 
Block_actuator
7
Remove back of Dynamixel MX-64 and replace with fan clamp d1.stl. Sunon fan snaps into place onto d1.stl. Use same 4 existing screws to attach clamp frame d1.stl to servo. Skip this step if fan implementation is not desired.

## Slide 15: Assembly
Block_actuator
8
Assemble main drive pulley onto actuator block sub-assembly as shown. M2 bolts should not interfere with servo rotation after assembly.
Parts | 
Sub-assembly from step 7 | 
b5.stl | 
M2.5, L7.5mm bolt | 
M2, L3mm bolt | 

## Slide 16: Assembly
Block_actuator
9
Assemble re-routing sub-assembly as shown above. It is suggested that a paper shim is used when press-fitting the top pin to ensure that the pulley is not pinched during assembly. Both pulleys should spin freely after assembly.
Parts | 
Pulley P1 (x2) | 
L3/8” pin J1 (x2) | 
b4_a.stl, b4_b.stl | 

## Slide 17: Assembly
Block_actuator
10
Finish assembling block actuator sub-assembly as shown above. Any bolt/nut pairing of size in close approximation to 2-56 can also be used here. Spectra tendon should be secured to the pulley at one of the two anchor holes (we use a no-slip, improved clinch knot) and wound clockwise, then up and through the pulleys in the sub-assembly from step 9.
Parts | 
Motor sub-assembly from step 8 | 
Tendon-routing sub-assembly from step 9 | 
2-56 L3/4” machine bolt/nut (x2) | 
Spectra Tendon ~8in (~200mm) | 

## Slide 18: Assembly
Pulley Blocks
11
Assemble the drive pulley block as shown above. Shorter steel pins can be used if desired, but pins must be longer than overall thickness of drive pulley sub-assembly. This sub-assembly should be attached to the other end of the Spectra tendon from step 10 with a no-slip knot.
Parts | 
b1.stl (x2) | 
Pulley P1 (x2) | 
L3/8” pin J1 (x3) | 

## Slide 19: Assembly
Pulley Blocks
12
Assemble the sets of pulley blocks as shown above. Ensure that all pulleys can spin freely. Use a paper shim during assembly with b2.stl as done in step 9 to avoid pinching.
x2
Parts | 
b2.stl (x2) | 
Pulley P1 (x2) | 
L3/8” pin J1 (x2) | 

## Slide 20: Assembly
Pulley Blocks
13
Assemble 2 sets of differential pulley blocks as shown above.
x2
Parts | 
b3.stl (x3) | 
Pulley P1 (x4) | 
L3/8” pin J1 (x6) | 

## Slide 21: Assembly
Flexure-Base Fingers
14
For pivot-base fingers, skip to step 18. Use a shim as done in steps 9 and 12 to ensure that nylon pulley spins freely at finger base
x4
Parts | 
Flexure-base Finger (x4) | 
Pulley P1 (x4) | 
L5/8” pin J2 (x12) | 

## Slide 22: Assembly
Flexure-Base Fingers Top
15
Insert fingers into top plate from above as illustrated in the figures. Fingers are inserted in at an angle and then tilted up into place. Finger base should lie flush with plate a2.stl
Parts | 
Finger sub-assembly from step 14 (x4) | 
a1_flexure.stl | 

## Slide 23: Assembly
Flexure-Base Fingers Top
16
Use socket cap screws and standoffs to fully assemble the top flexure-base sub-assembly. Plates a1_flexure.stl and a2.stl should sandwich and immobilize the finger bases
Parts | 
Sub-assembly from step 15 | 
a2.stl | 
Female standoffs S1 (x4) | 
8-32 Socket Cap Screws (x4) | 

## Slide 24: Assembly
Flexure-Base Fingers Top
17
Each tendon runs from the back of the fingertip, down through the finger base, across the differential block from step 13, and back up through to the tip of the finger on the same side.
Use tendon to affix differential sub-assembly blocks to the sub-assembly made in the last step. Tendon length should be set such that it is taut when the fingers are at rest. Tendon tied off to small nut at back of finger.
Parts | 
Sub-assembly from step 16 | 
Sub-assembly from step 13 (x2) | 
Spectra Tendon ~8in (200mm) (x2) | 

## Slide 25: Assembly
Pivot-Base Fingers
18
Assemble re-routing pins to fingers as shown in figures above.
Parts | 
Pivot-base Finger (x4) | 
L5/8” pin J2 (x8) | 

## Slide 26: Assembly
Pivot-Base Fingers
19
Assemble pivot base sub-assembly as shown. Use shim when press-fitting the pin and pulley to ensure that the pulley spins freely after assembly.
Parts | 
c1.stl (x2) | 
Pulley P1 (x2) | 
L5/8” pin J2 (x2) | 

## Slide 27: Assembly
Pivot-Base Fingers TOP
20
Assemble top pivot base plate as shown above. The bottoms of the finger pivot bases should fit flush with the top plate. The interior sides of a1_pivot.stl may need to be filed down for a proper fit.
Parts | 
Sub-assembly from step 19 (x4) | 
a1_pivot.stl | 

## Slide 28: Assembly
21
Assemble fingers onto top plate as shown above. Ends of torsion spring align with opening on finger and slot in finger base. It’s easiest to align/position the spring first and then press the joint pin J3 through the pivot base c1.stl and the finger base.
Cut off excess torsion spring ends when done. Ensure that the fingers rotate without friction.
Pivot-Base Fingers TOP
Parts | 
Sub-assembly from step 20 | 
Pivot-base finger sub-assemblies from step 18 | 
L1” pin J3 (x4) | 
Torsion Spring (x4) | 

## Slide 29: Assembly
22
Use socket cap screws and standoffs to fully assemble the top flexure-base sub-assembly. Plates a1_pivot.stl and a2.stl should sandwich and immobilize the finger bases
Pivot-Base Fingers TOP
Parts | 
Sub-assembly from step 21 | 
a2.stl | 
Female standoffs S1 (x4) | 
8-32 Socket Cap Screws (x4) | 

## Slide 30: Assembly
23
Use tendon to affix differential sub-assembly blocks to the sub-assembly made in the last step. Tendon length should be set such that it is taut when the fingers are at rest. Tendon tied off to small nut at back of finger.
Pivot-Base Fingers TOP
Parts | 
Sub-assembly from step 22 | 
Sub-assembly from step 13 (x2) | 
Spectra Tendon ~8in (200mm) (x2) | 

## Slide 31: Assembly
24
Attach drive pulley block to the actuator block with Spectra tendon. Tendon should tie off on topmost pin in sub-assembly from step 11 and main drive pulley. The improved clinch knot is suggested as a no-slip knot in this situation. Do not worry about zero-ing the tendon at this step.
Final tendon routing
Parts | 
Sub-assembly from step 10 | 
Sub-assembly from step 11 | 

## Slide 32: Assembly
25
Final Tendon Routing
Transmission Diagram
Left Fingers
Right Fingers
Actuator
Parts | 
Sub-assembly from step 24 | 
Sub-assembly from step 17 (for Flexure-base design) or step 23 (for pivot-base design) | 
Sub-assembly from step 12 (x2) | 
Spectra Tendon ~8in (200mm) | 
Final tendon runs between the differential blocks from step 13 and through the pulley blocks from step 12 and main drive block from step 11. The tendon length is approximately 14cm (5.5”) between the two termination points. This tendon will be taut once the hand is fully assembled, and the fingers are at rest.

## Slide 33: Assembly
25
Note that the base pulley blocks can be inserted into the bottom base from above, as shown above. This may help in the process of achieving the appropriate tendon length between the differential blocks.
Bend the fingers in order to generate slack in the tendon.
Final Tendon Routing
a3.stl

## Slide 34: Assembly
26
Use remaining socket screws to clamp the entire assembly together in place. The actuator block sub-assembly from step 10 should fit snugly
Final Assembly – Flexure base

## Slide 35: Assembly
27
Use remaining socket screws to clamp the entire assembly together in place. The actuator block sub-assembly from step 10 should fit snugly
Final Assembly – Pivot base

## Slide 36: Assembly
28
Optional shell snaps together from two sides, as shown above. It may help to pre-loosen either the top or bottom set of socket screws to allow the shells to slide together more easily.
Final Assembly – Shell
d2_a.stl
d2_b.stl

## Slide 37: Post-Assembly
29
Servo Zero-ing
Remove the M2 bolts from the servo pulley
Loosen, but do not remove, the central M2.5 bolt, such that the servo pulley can spin freely
Connect the Dynamixel and (in position mode) move it to its zero encoder position
By hand, turn the servo pulley until the tendon between the pulley and the main drive block is as taut as possible
Re-attach the M2 bolts and tighten the servo pulley
Consult the main documentation for suggested software and control methodologies.
You may need to adjust tendon lengths (especially the tendon running between the differential pulley blocks) to optimize operation.