## Slide 1
OpenHand
Model T
Version 0.5
Assembly Instructions
Last updated: May 23, 2013

## Slide 2: Parts List 1/2 (Flexure Base)
Part Name | Quantity | Usage | Vendor
a1.stl | 1 | Top Keeper Plate | 3D Print
a2.stl | 1 | Top Plate | 3D Print
a3.stl | 1 | Bottom Plate | 3D Print
a4.stl | 1 | Bottom Keeper Plate | 3D Print
b1.stl | 2 | Drive Pulley Block | 3D Print
b2.stl | 2 | Routing Base Block | 3D Print
b3.stl | 4 | Differential Block | 3D Print
b4_a.stl, b4_b.stl | 1 | Servo Block | 3D Print
b5.stl | 1 | Servo Pulley | 3D Print
d1.stl | 1 | Sunon Fan Clamp* | 3D Print
d2_a.stl, d2_b.stl | 1 | Case Shell* | 3D Print
finger.stl | 4 | Finger Molds | 3D Print
* optional

## Slide 3: Parts List 2/2 (Flexure Base)
Part Name | Quantity | Usage | Vendor
Robotis MX-64 Dynamixel | 1 | Actuator | Robotis [link]
Ø1/8”, L3/8” steel dowel pin (J1) | 13 | Support Pin | McMaster [98381A470]
Ø1/8”, L5/8” steel dowel pin (J2) | 12 | Support Pin | McMaster [98381A472]
Ø3/8”, Wd1/8” nylon pulley (P1) | 12 | Tendon Routing | McMaster [3434T31]
Ø1/4”, L2-1/2” zinc-plated female standoff (S1) | 4 | Support | McMaster [92474A029]
Socket Cap Screw 8-32, L3/4” | 8 | Fastener | McMaster [91253A197]
M2.5, L7.5mm bolt | 1 | Fastener | Provided w/ Dynamixel
M2, L3mm bolt | 2 | Fastener | McMaster [91292A003]
2-56, L3/4” bolt/nut | 2 | Fastener | McMaster [92196A084]
PMC-780 Urethane | 1 | Finger Joint Urethane | Smooth-On [link]
Vytaflex 30 Urethane | 1 | Finger Pad Urethane | Smooth-On [link]
Sunon 25x10mm 12VDC Fan | 1 | Cooling Fan* | Digikey [link]
Power Pro Spectra | 1 | Tendon | Amazon [link]
* optional

## Slide 4: Parts List 1/2 (Pivot Base)
Part Name | Quantity | Usage | Vendor
a1.stl | 1 | Top Keeper Plate | 3D Print
a2_pivot.stl | 1 | Top Plate | 3D Print
a3.stl | 1 | Bottom Plate | 3D Print
a4.stl | 1 | Bottom Keeper Plate | 3D Print
b1.stl | 2 | Drive Pulley Block | 3D Print
b2.stl | 2 | Routing Base Block | 3D Print
b3.stl | 4 | Differential Block | 3D Print
b4_a.stl, b4_b.stl | 1 | Servo Block | 3D Print
b5.stl | 1 | Servo Pulley | 3D Print
c1.stl | 4 | Finger Pivot Base | 3D Print
d1.stl | 1 | Sunon Fan Clamp* | 3D Print
d2_a.stl, d2_b.stl | 1 | Case Shell* | 3D Print
finger_pivot.stl | 4 | Finger Molds | 3D Print
* optional

## Slide 5: Parts List 2/2 (Pivot Base)
Part Name | Quantity | Usage | Vendor
Robotis MX-64 Dynamixel | 1 | Actuator | Robotis [link]
Ø1/8”, L3/8” steel dowel pin (J1) | 13 | Support Pin | McMaster [98381A470]
Ø1/8”, L5/8” steel dowel pin (J2) | 12 | Support Pin | McMaster [98381A472]
Ø1/4”, L1” steel dowel pin (J3) | 4 | Joint Pin | McMaster [98381A542]
Ø3/8”, Wd1/8” nylon pulley (P1) | 12 | Tendon Routing | McMaster [3434T31]
Ø1/4”, L2-1/2” zinc-plated standoff | 4 | Support | McMaster [92474A029]
Socket Cap Screw 8-32, L3/4” | 8 | Fastener | McMaster [91253A197]
M2.5, L7.5mm bolt | 1 | Fastener | Provided w/ Dynamixel
M2, L3mm bolt | 2 | Fastener | McMaster [91292A003]
2-56, L3/4” bolt/nut | 2 | Fastener | McMaster [92196A084]
Torsion Spring, Ø0.34”, 0.028” wire diameter, 180˚, left-hand wound | 4 | Joint Return Spring | McMaster [9271K605]
PMC-780 Urethane | 1 | Finger Joint Urethane | Smooth-On [link]
Vytaflex 30 Urethane | 1 | Finger Pad Urethane | Smooth-On [link]
Sunon 25x10mm 12VDC Fan | 1 | Cooling Fan* | Digikey [link]
Power Pro Spectra | 1 | Tendon | Amazon [link]
* optional

## Slide 6: Part Preparation
Finger Molding
Consult DDM (Dieless Deposition Manufacturing) guide for further details on pouring/preparing the joints and pads for fingers
1
finger.stl
finger_pivot.stl

## Slide 7: Part Preparation
Tendon Routing
2
Drill tendon routing holes such that tendon will run tangent to inserted pin. Minimize contact between tendon and ABS but ensure that tendon runs freely. Use helper_jig.stl to aid in positioning. Hole should be drilled perpendicular to routing surface.
Ø 1.5±0.5 mm
finger.stl (x4)
finger_pivot.stl (x4)

## Slide 8: Part Preparation
Surface Filing/Deburring
3
File down and deburr bearing surfaces as indicated above. Ensure that no support material remains, if applicable. Complementary piece (ie. pulley, finger) should slide in freely.
b4_a.stl
b4_b.stl
b2.stl (x2)
finger.stl (x4)
c1.stl (x4)

## Slide 9: Part Preparation
Reaming (1/8” pin holes)
4
Use Ø0.1240” reamer to prepare pin holes as indicated above. This step can be skipped in lieu of precise 3D printer calibration and parameter selection, but manual reaming is the recommended approach.
b4_a.stl
b4_b.stl
finger.stl (x4)
finger_pivot.stl (x4)
b1.stl (x2)
b2.stl (x2)
b3.stl (x4)
c1.stl (x4)

## Slide 10: Part Preparation
Reaming (Pivot Bases)
5
Use Ø0.2490” reamer to prepare pin holes on pivot bases c1.stl, and Ø0.2510” reamer to prepare pin holes on the corresponding fingers finger_pivot.stl. Finger should spin freely and loosely on a Ø0.25” steel pin
Ø 0.2510 “
Ø 0.2490 “
finger_pivot.stl (x4)
c1.stl (x4)

## Slide 11: Assembly
Block_actuator
6
Remove back of Dynamixel MX-64 and replace with fan clamp d1.stl. Sunon fan snaps into place. Use same existing screws to attach clamp frame d1.stl to servo. Skip this step is fan implementation is not desired.
Parts:
Dynamixel MX-64
d1.stl
Sunon 12VDC fan

## Slide 12: Assembly
Block_actuator
7
Assemble main drive pulley onto actuator block sub-assembly as shown. M2 bolts should not interfere with servo rotation after assembly.
Parts:
Sub-assembly from step 6
b5.stl
M2.5, L7.5mm bolt
M2, L3mm bolt

## Slide 13: Assembly
Block_actuator
8
Assemble re-routing sub-assembly as shown above. It is suggested that a paper shim is used when press-fitting the top pin to ensure that the pulley is not pinched.
Parts:
Pulley P1 (x2)
L3/8” pin J1 (x2)
b4_a.stl
b4_b.stl

## Slide 14: Assembly
Block_actuator
9
Finish assembly block actuator sub-assembly as shown above. Any bolt/nut pairing of size in close approximation to 2-56 can also be used here. Ensure that both nylon pulleys spin freely.
Parts:
Sub-assembly from step 7
Sub-assembly from step 8
2-56 L3/4” machine bolt/nut (x2)

## Slide 15: Assembly
Pulley Blocks
10
Assemble the drive pulley block as shown above. Shorter steel pins can be used if desired, but pins must be longer than overall thickness of drive pulley sub-assembly
Parts:
b1.stl (x2)
Pulley P1 (x2)
L3/8” pin J1 (x3)
x1

## Slide 16: Assembly
Pulley Blocks
11
Assemble the sets of pulley blocks as shown above. Ensure that all pulleys can spin freely. Use a paper shim during assembly with b2.stl to avoid pinching.
Parts:
b2.stl (x2)
Pulley P1 (x2)
L3/8” pin J1 (x2)
x2

## Slide 17: Assembly
Pulley Blocks
12
Assemble 2 sets of differential pulley blocks as shown above.
Parts:
b3.stl (x4)
Pulley P1 (x4)
L3/8” pin J1 (x6)
x2

## Slide 18: Assembly
Flexure-Base Fingers
13
For pivot-base fingers, skip to step 17. Use a shim as done in steps 8 and 11 to ensure that nylon pulley spins freely at finger base
Parts:
finger.stl (x4)
Pulley P1 (x4)
L5/8” pin J2 (x12)
x4

## Slide 19: Assembly
Flexure-Base Fingers Top
14
Insert fingers into top plate from above as illustrated in the figures. Finger base should lie flush with plate a2.stl
Parts:
Finger sub-assembly from step 13 (x4)
a2.stl

## Slide 20: Assembly
Flexure-Base Fingers Top
15
Use socket cap screws and standoffs to fully assemble the top flexure-base sub-assembly. Plates a1.stl and a2.stl should sandwich and immobilize the finger bases
Parts:
Sub-assembly from step 14
a1.stl
Female standoffs S1 (x4)
8-32 Socket Cap Screws (x4)

## Slide 21: Assembly
Flexure-Base Fingers Top
16
Use tendon to affix differential sub-assembly blocks to the sub-assembly made in the last step. Tendon length should be set such that it is taut when the fingers are at rest. Tendon tied off to small nut at back of finger.
Parts:
Sub-assembly from step 15
Sub-assemblies from step 12 (x2)
Spectra Tendon ~8” (x2)

## Slide 22: Assembly
Pivot-Base Fingers
17
Assemble re-routing pins to fingers as shown in figures above.
Parts:
finger_pivot.stl (x4)
L5/8” pin J2 (x8)

## Slide 23: Assembly
Pivot-Base Fingers
18
Assemble pivot base sub-assembly as shown. Use shim when press-fitting the pin and pulley to ensure that the pulley spins freely after assembly.
Parts:
c1.stl (x2)
L5/8” pin J2 (x2)
Pulley P1 (x2)

## Slide 24: Assembly
Pivot-Base Fingers TOP
19
Assemble top pivot base plate as shown above. The finger pivot bases should fit flush with the top plate.
Parts:
Sub-assemblies from step 18 (x4)
a2_pivot.stl

## Slide 25: Assembly
20
Assemble fingers onto top plate as shown above. Ends of torsion spring align with opening on finger and slot in finger base. Cut off excess torsion spring ends when done. Ensure that the fingers rotate without friction.
Parts:
Sub-assembly from step 19
Finger sub-assemblies from step 17
Steel pin J3 (x4)
Torsion spring (x4)
Pivot-Base Fingers TOP

## Slide 26: Assembly
21
Use socket cap screws and standoffs to fully assemble the top flexure-base sub-assembly. Plates a1.stl and a2_pivot.stl should sandwich and immobilize the finger bases
Pivot-Base Fingers TOP
Parts:
Sub-assembly from step 20
a1.stl
Female standoffs S1 (x4)
8-32 Socket Cap Screws (x4)

## Slide 27: Assembly
22
Use tendon to affix differential sub-assembly blocks to the sub-assembly made in the last step. Tendon length should be set such that it is taut when the fingers are at rest. Tendon tied off to small nut at back of finger.
Pivot-Base Fingers TOP
Parts:
Sub-assembly from step 21
Sub-assemblies from step 12 (x2)
Spectra Tendon ~8” (x2)

## Slide 28: Assembly
23
Attach drive pulley block to the actuator block with Spectra tendon. Tendon should tie off on topmost pin in sub-assembly from step 10 and main drive pulley. The improved clinch knot is suggested as a no-slip knot in this situation
Pivot-Base Fingers TOP
* Do not worry about zero-ing the tendon in this step.
Parts:
Sub-assembly from step 9
Sub-assembly from step 10
Spectra Tendon ~8”

## Slide 29: Assembly
24
Final tendon runs between the differential blocks from step 12 and through the pulley blocks from step 11 and main drive block from step 10. The tendon length is approximately 14cm (5.5”) and should be taut with the fingers at rest.
Final Tendon Routing
Transmission Diagram
Left Fingers
Right Fingers
Actuator
Parts:
Sub-assembly from step 23
Sub-assembly from step 22 or step 16
Spectra Tendon ~8”

## Slide 30: Assembly
25
Note that the base pulley blocks can be inserted into the bottom base from above, as shown above. This may help in the process of achieving the appropriate tendon length between the differential blocks.
Final Tendon Routing

## Slide 31: Assembly
25
Use remaining socket screws to clamp the entire assembly together in place. The actuator block sub-assembly from step 9 should fit snugly
Final Assembly – Flexure base

## Slide 32: Assembly
26
Use remaining socket screws to clamp the entire assembly together in place. The actuator block sub-assembly from step 9 should fit snugly
Final Assembly – Pivot base

## Slide 33: Assembly
27
Optional shell snaps together from two sides, as shown above. It may help to pre-loosen either the top or bottom set of socket screws to allow the shells to slide together more easily.
Final Assembly – Shell

## Slide 34: Post-Assembly
28
Servo Zero-ing
Remove the M2 bolts from the servo pulley
Loosen, but do not remove, the central M2.5 bolt, such that the servo pulley can spin freely
Connect the Dynamixel and (in position mode) move it to its zero encoder position
By hand, turn the servo pulley until the tendon between the pulley and the main drive block is as taut as possible
Re-attach the M2 bolts and tighten the servo pulley