## Slide 1
OpenHand
Model T42
Version 0.3
Assembly Instructions
Last updated: November 28, 2013
Flexure Base
Pivot Base

## Slide 2: Parts List (Flexure Base)
Part Name | Quantity | Usage | Vendor | 
a1_flexure.stl | 1 | Top Plate | 3D Print | 
a2.stl | 1 | Top Keeper Plate | 3D Print | 
a3.stl | 1 | Bottom Plate | 3D Print | 
a4.stl | 1 | Bottom Keeper Plate | 3D Print or Lasercut | 
b1.stl | 1 | Central Coupler | 3D Print | 
b2.stl | 2 | Servo Pulley | 3D Print | 
finger_flexure_print.stl | 2 | Finger Molds – Breakaway | 3D Print | 
finger_ff_A.stl, finger_ff_B.stl, finger_ff_C.stl, shell_ff_A.stl, shell_ff_B.stl, shell_ff_C.stl | 2 | Finger Molds - Multipart | 3D Print | 
Power Pro Spectra | 1 | Tendon | Amazon [link] | 
PMC-780 Urethane | 1 | Finger Joint Urethane | Smooth-On [link] | 
Vytaflex 30 Urethane | 1 | Finger Pad Urethane | Smooth-On [link] | 
* optional

## Slide 3: Parts List (Flexure Base)
Part Name | Quantity | Usage | Vendor | 
Robotis RX-28 Dynamixel | 2 | Actuator | Robotis [link] | 
Ø1/8”, L1-1/4” steel dowel pin (J1) | 4 | Support Pin | McMaster [98381A477] | 
Ø1/8”, L5/8” steel dowel pin (J2) | 2 | Support Pin | McMaster [98381A472] | 
Ø3/8”, Wd1/8” nylon pulley (P1) | 6 | Tendon Routing | McMaster [3434T31] | 
M2.5, L5mm bolt | 2 | Fastener | Provided w/ Dynamixel McMaster [92290A055] | 
M2, L5mm bolt | 4 | Fastener | McMaster [91290A012] | 
Socket Cap Screw 8-32, L3/4” | 8 | Fastener | McMaster [91253A197] | 
Ø1/4”, L1-1/2” zinc-plated female standoff (S1) | 4 | Support | McMaster [93330A482] | 
Torsion Spring, Ø0.34”, 0.028” wire diameter, 180˚, left-hand wound | 4 | Joint Return Spring | McMaster [9271K605] | 
* optional

## Slide 4: Parts List (Pivot Base)
Part Name | Quantity | Usage | Vendor | 
a1_pivot.stl | 1 | Top Plate | 3D Print | 
a2.stl | 1 | Top Keeper Plate | 3D Print | 
a3.stl | 1 | Bottom Plate | 3D Print | 
a4.stl | 1 | Bottom Keeper Plate | 3D Print or Lasercut | 
b1.stl | 1 | Central Coupler | 3D Print | 
b2.stl | 2 | Servo Pulley | 3D Print | 
c1.stl | 2 | Finger Pivot Base | 3D Print | 
finger_pivot_print.stl | 2 | Finger Molds – Breakaway | 3D Print | 
finger_fp_A.stl, finger_fp_B.stl, shell_fp_A.stl, shell_fp_B.stl, shell_fp_C.stl | 2 | Finger Molds - Multipart | 3D Print | 
* optional

## Slide 5: Parts List (Pivot Base)
Part Name | Quantity | Usage | Vendor | 
Robotis RX-28 Dynamixel | 2 | Actuator | Robotis [link] | 
Ø1/8”, L1-1/4” steel dowel pin (J1) | 10 | Support Pin | McMaster [98381A477] | 
Ø3/8”, Wd1/8” nylon pulley (P1) | 6 | Tendon Routing | McMaster [3434T31] | 
M2.5, L5mm bolt | 2 | Fastener | Provided w/ Dynamixel McMaster [92290A055] | 
M2, L5mm bolt | 4 | Fastener | McMaster [91290A012] | 
Socket Cap Screw 8-32, L3/4” | 8 | Fastener | McMaster [91253A197] | 
Ø1/4”, L1-1/2” zinc-plated female standoff (S1) | 4 | Support | McMaster [93330A482] | 
Power Pro Spectra | 1 | Tendon | Amazon [link] | 
PMC-780 Urethane | 1 | Finger Joint Urethane | Smooth-On [link] | 
Vytaflex 30 Urethane | 1 | Finger Pad Urethane | Smooth-On [link] | 
* optional

## Slide 6: Part Preparation
Finger Molding
Consult DDM (Dieless Deposition Manufacturing) guide for further details on pouring/preparing the joints and pads for fingers
1
finger_flexure_print.stl
finger_pivot_print.stl

## Slide 7: Part Preparation
Ø 1.5±0.5 mm
finger_flexure_print.stl (x4)
Tendon Routing
2
Drill tendon routing holes such that tendon will run tangent to inserted pin. Minimize contact between tendon and ABS but ensure that tendon runs freely. For the pivot base design, the fingers also have a torsional spring mounting hole to be drilled as shown.
finger_pivot_print.stl (x4)

## Slide 8: Part Preparation
Tendon Routing (2/2)
3
Use helper_jig.stl to aid in positioning and orientation during drilling if desired. Routing holes should be drilled perpendicular to hole surface. The fingers are designed such that for each routing hole, there is at least one feature surface that is perpendicular to the direction of drilling, as shown above. It is ideal to minimize the diameter of the tendon routing holes if possible.
helper_jig.stl

## Slide 9: Part Preparation
Surface Filing/Deburring
4
File down and deburr bearing surfaces as indicated above. Ensure that no support material remains, if applicable. Complementary piece (ie. pulley, finger) should slide in freely.
finger_flexure_print.stl (x2)
c1.stl (x2)

## Slide 10: Part Preparation
Reaming (1/8” pin holes)
5
Use Ø0.1240” reamer to prepare pin holes as indicated above. This step can be skipped in lieu of precise 3D printer calibration and parameter selection, but manual reaming is the recommended approach.
c1.stl (x2)
finger_flexure.stl (x2)
finger_pivot.stl (x2)

## Slide 11: Part Preparation
Reaming (Pivot Bases)
6
Use Ø0.2490” reamer to prepare pin holes on pivot bases c1.stl, and Ø0.2510” reamer to prepare pin holes on the corresponding fingers finger_pivot.stl. Finger should spin freely and loosely on a Ø0.25” steel pin
Ø 0.2510 “
Ø 0.2490 “
finger_pivot.stl (x2)
c1.stl (x2)

## Slide 12: Assembly
Block_actuator
7
Remove back of Dynamixel RX-28’s. The two Dynamixel servo’s snap onto the coupler piece b1.stl as shown above. Connect the two Dynamixel servos in a daisy-chain configuration.
Parts | 
Dynamixel RX-28 (x2) | 
b1.stl | 

## Slide 13: Assembly
Parts | 
Sub-assembly from step 7 | 
b2.stl (x2) | 
M2.5 L5mm bolt (x2) | 
M2 L5mm (x4) | 
Block_actuator
8
Assemble main drive pulleys onto actuator block sub-assembly as shown. Do not worry about zero-position of servo at this time.
(Optional): It may be beneficial to attach one end of the tendons to the pulleys at this point. Use enough tendon to wrap around the pulley fully at least once and also reach the end of the fingertips after routing.

## Slide 14: Assembly
Block_actuator
9
Assemble main drive pulleys onto actuator block sub-assembly as shown. Do not worry about zero-position of servo at this time.
Parts | 
Sub-assembly from step 8 | 
a3.stl | 
a4.stl | 
Ø1/4”, L1-1/2” standoffs S1 (x4) | 
Socket Cap Screw 8-32, L3/4” (x4) | 

## Slide 15: Assembly
Flexure-Base Fingers
10
For pivot-base fingers, skip to step 12. Use a shim while press-fitting the pins to help ensure that nylon pulley spins freely at finger base
Parts | 
Flexure-based finger (x2) | 
Pulley P1 (x6) | 
L1-1/4” pin J1 (x10) | 

## Slide 16: Assembly
Flexure-Base Fingers Top
11
Insert fingers into top plate from above as illustrated in the figures. Finger base should lie flush with plate a1_flexure.stl
Parts | 
Finger sub-assembly from step 10 (x2) | 
a1_flexure.stl | 

## Slide 17: Assembly
Pivot-Base Fingers
12
Assemble pivot base sub-assembly as shown. Use shim when press-fitting the pin and pulley to ensure that the pulley spins freely after assembly.
Parts | 
c1.stl (x2) | 
L5/8” pin J2 (x2) | 
Pulley P1 (x2) | 

## Slide 18: Assembly
Pivot-Base Fingers TOP
13
Assemble top pivot base plate as shown above. The finger pivot bases should fit flush with the top plate.
Parts | 
Sub-assembly from step 12 (x2) | 
a1_pivot.stl | 

## Slide 19: Assembly
Pivot-Base Fingers TOP
14
Install the torsion spring as shown above. Position the finger appropriately in c1.stl, and then slide the ¼” pin in place to secure this sub-assembly for each finger.
Parts | 
Sub-assembly from step 13 | 
Pivot-based Finger (x2) | 
Torsion spring (x2) | 
L1-1/4” pin J1 (x4) | 

## Slide 20: Assembly
15
Use remaining socket screws to clamp the entire assembly together in place. The actuator block sub-assembly from step 9 should fit snugly
Final Assembly – Flexure base
Parts | 
Top sub-assembly from step 11 | 
Base sub-assembly from step 9 | 
Socket Cap Screw 8-32, L3/4” (x4) | 

## Slide 21: Assembly
16
Use remaining socket screws to clamp the entire assembly together in place. The actuator block sub-assembly from step 9 should fit snugly
Final Assembly – Pivot base
Parts | 
Top sub-assembly from step 14 | 
Base sub-assembly from step 9 | 
Socket Cap Screw 8-32, L3/4” (x4) | 

## Slide 22: Tendon Routing
17
Tendons for flexure-based fingers run from the drive pulleys, through the top plate, across the 3 pulleys in the finger base, and through the finger routing ports, anchoring at the back of the fingertip, as shown above.
There should be enough tendon to leave slack after tying both ends. It is probably easiest to thread the tendon up from the servo to the fingertip.
Flexure-Base Fingers

## Slide 23: Tendon Routing
18
Tendons for flexure-based fingers run from the drive pulleys, through the top plate, across the pulley in the finger base, over the finger end, and through the finger routing ports, anchoring at the back of the fingertip, as shown above.
There should be enough tendon to leave slack after tying both ends.
Pivot-Base Fingers

## Slide 24: Post-Assembly
19
Servo Zero-ing
Remove the M2 bolts from the servo pulley
Loosen, but do not remove, the central M2.5 bolt, such that the servo pulley can spin freely
Connect the Dynamixel and (in position mode) move it to its zero encoder position
By hand, turn the servo pulley until the tendon between the pulley and the main drive block is as taut as possible
Re-attach the M2 bolts and tighten the servo pulley
Repeat for other servo